## Slide 1
0
2026 ASCE–EWRI Watershed Management Conference
Curve Number Hydrology and Remote Sensing Task Committees
Modern Curve Number Hydrology
Theory, spatial estimation, and Earth Observation applications
DURATION
Four hours
FORMAT
Lecture and three computational labs
CREDIT
4.0 PDH for the full workshop
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
John J. Ramirez-Avila, Mississippi State University | Saurav Kumar, Arizona State University
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- docs/V3_BLUEPRINT.md
- 2026 ASCE–EWRI workshop program

## Slide 2
Workshop instructors
The workshop integrates curve-number hydrology, spatial data, and engineering interpretation.
0
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
JJ
John J. Ramirez-Avila
Mississippi State University
Curve-number theory, rainfall–runoff interpretation, and the reporting implications of calibration and compositing.
SK
Saurav Kumar
Arizona State University
Earth Observation, watershed-scale estimation, temporal change, and reproducible computational workflows.
Participants may use verified reference datasets or apply the same analytical framework through Earth Engine to a selected watershed.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- docs/V3_BLUEPRINT.md
- docs/PARTICIPANT_GUIDE.md

## Slide 3
Workshop schedule
Three linked modules move from theory to spatial estimation and interpretation.
0
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
0:00
Welcome and orientation
10 min
0:10
Foundations: rainfall, runoff, and curve number
40 min
0:50
Lab 1 and report-out
30 min
1:20
Break
15 min
1:35
Earth Observation and spatial estimation
25 min
2:00
Lab 2 and report-out
45 min
2:45
Break
15 min
3:00
Change, uncertainty, and Lab 3
45 min
3:45
Reporting synthesis and close
15 min
4:00
End
15 min
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- content/workshop.mjs
- docs/INSTRUCTOR_RUNBOOK.md

## Slide 4
Learning objectives
0
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
1
Explain the governing relation
Relate rainfall, initial abstraction, retention, runoff, curve number, and the initial-abstraction ratio.
2
Estimate CN from spatial data
Combine watershed boundaries, land cover, and hydrologic soil group with explicit provenance.
3
Evaluate methodological uncertainty
Compare observed change with hydrologic condition, soil coverage, calibration, and compositing choices.
4
Prepare a reproducible statement
Report the parameter, data sources, assumptions, spatial coverage, and evidence supporting interpretation.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- docs/V3_BLUEPRINT.md
- notebooks/01–03 participant objectives

## Slide 5
Two reference watersheds anchor the analysis
Long-record USGS gages provide contrasting physiographic and hydrologic settings.
0
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
USGS NWIS and NLDI; workshop data registry
Difficult Run near Great Falls, Virginia
USGS 01646000
Drainage area
57.8 square miles
Physiography
Piedmont
Record begins
1935
Workshop role
Complete spatial and gage analysis
Accotink Creek near Annandale, Virginia
USGS 01654000
Drainage area
23.9 square miles
Physiography
Coastal Plain
Record begins
1947
Workshop role
Contrasting fitted behavior
The reference datasets support the complete analytical sequence; Earth Engine extends the same method to a participant-selected watershed.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- data/sites.csv
- USGS NWIS
- USGS NLDI

## Slide 6
1
FOUNDATIONS · THEORY AND CALIBRATION
A curve number is inferred from rainfall–runoff behavior; it is not a directly observed property of a pixel.
The spatial inputs inform parameter estimation. The runoff relation, calibration convention, and observed response determine its interpretation.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- NRCS NEH-630 Chapters 9 and 10 (2004)

## Slide 7
Curve number is inferred from storm response
Measured rainfall and runoff provide the evidence used to evaluate an assigned table value.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
USGS NWIS; events_01646000.csv; cnkit 1.1.0
Difficult Run storm events
570 separated events · 1990–2026
Parameter estimation
NRCS runoff relation
Observed variables
Rainfall P and runoff Q
Model parameters
Curve number CN and λ
Asymptotic fit
CN∞ = 69.7
Table estimate
CN = 75.5
The fitted estimate is obtained from measured events; the table estimate is assigned from land cover, soil, and hydrologic condition.
Chart: Runoff, in
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- data/events_01646000.csv
- USGS NWIS
- cnkit 1.1.0 fit_asymptotic

## Slide 8
The runoff equation contains two linked parameters
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Rainfall, P
Observed storm depth for the event.
Initial abstraction, Iₐ = λS
Loss before runoff begins; λ is part of the calibration.
Potential retention, S
S = 1000/CN − 10 inches.
Direct runoff, Q
Q = (P − Iₐ)² / (P − Iₐ + S) for P > Iₐ; otherwise Q = 0.
Changing λ changes the curve-number scale. Report λ and CN together.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- NRCS NEH-630 Chapter 10 (2004), equations 10-1 and 10-12

## Slide 9
Lambda and curve number form a calibration pair
Changing one without converting the other changes the model response.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NEH-630 Ch. 10; Woodward et al. (2003)
Conventional formulation
Initial-abstraction ratio λ = 0.20
Curve number
75.5
Three-inch storm
0.988 in runoff
Calibration basis
NEH/TR-55 tables
Retention
S = 3.245 in
Alternative formulation
Initial-abstraction ratio λ = 0.05
Converted curve number
66.0
Three-inch storm
0.953 in runoff
Calibration basis
Empirical conversion
Interpretation
A different CN scale
A reported curve number is incomplete unless its initial-abstraction convention is stated.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- NRCS NEH-630 Chapter 10 (2004)
- Woodward et al. 2003, DOI 10.1061/40685(2003)308

## Slide 10
Six choices govern a spatial curve-number estimate
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Land cover
Product, class system, vintage, and spatial resolution.
Hydrologic soil group
Source, map-unit interpretation, dual groups, and coverage.
Hydrologic condition
Poor, fair, or good condition changes the lookup value.
Initial abstraction
The selected λ must be paired with the curve-number calibration.
Compositing convention
Distributed runoff, area-weighted CN, or area-weighted S.
Spatial completeness
Unmapped land-cover or soil area belongs beside the result.
These choices are methodological inputs, not incidental software settings.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- NRCS NEH-630 Chapters 7, 9, and 10
- USDA TR-55 (1986)

## Slide 11
Compositing order changes runoff
One inch of rainfall over 60% connected impervious cover and 40% woods.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NEH-630 Ch. 9; TR-55 Worksheet 2; cnkit calculation
Three valid calculations
CN 98 impervious · CN 55 woods
Distributed runoff
0.4745 in
Area-weighted CN
0.0949 in
Area-weighted S
0.0277 in
Maximum ratio
17×
Why the results diverge
The wooded subarea has Iₐ = 1.64 in
Storm depth
1.00 in
Distributed sequence
Compute Q, then average
Lumped sequence
Average parameter, then Q
Engineering choice
Document the representation
The arithmetic is correct in each case; the calculations represent different spatial models.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- USDA TR-55 Worksheet 2
- NRCS NEH-630 Chapter 9
- notebooks/01_Understand_the_Curve_Number.ipynb

## Slide 12
Lab 1 · Understand and audit the equation
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Run the setup and comparison
Open Notebook 01, execute the reference calculations, and inspect the three-inch storm table.
Evaluate the lambda pair
Explain why λ = 0.20 and λ = 0.05 require different curve-number scales.
Calculate the weighting example
Compare distributed runoff, weighted CN, and weighted S for the one-inch storm.
Prepare the report-out
Select a compositing convention and identify the evidence supporting that choice.
Working time: 20 minutes. Record the three runoff depths and one concise interpretation.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- notebooks/01_Understand_the_Curve_Number.ipynb

## Slide 13
1
LAB 1 · REPORT-OUT
Which compositing convention would you report for a heterogeneous watershed, and what evidence supports that choice?
State the calculation sequence, the resulting runoff depth, and the spatial representation implied by the method.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- notebooks/01_Understand_the_Curve_Number.ipynb

## Slide 14
Earth Observation supports spatial estimation
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Define the watershed
Use a verified boundary, USGS gage number, or outlet coordinates.
Measure land cover
Select the product, year, resolution, and class system explicitly.
Resolve hydrologic soil group
Link mapped soil units to HSG and quantify the area with no assignment.
Aggregate the joint distribution
Align land cover and soil spatially, then summarize observed class pairs.
Reference datasets provide verified outputs; Earth Engine applies the same sequence to a selected watershed.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- USGS NLDI
- Annual NLCD
- USDA Soil Data Access
- cnkit 1.1.0

## Slide 15
Marginal and joint distributions differ
The distinction is spatial association, not simply data volume.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
EPA StreamCat; USDA SDA; Annual NLCD; gNATSGO
Marginal distributions
Land-cover and soil percentages are separate
Spatial association
Not retained
Required assumption
Independent pairing
Computation
Cross all classes
Interpretation
Synthetic joint table
Joint spatial distribution
Land-cover–soil pairs share a location
Spatial association
Measured pixel by pixel
Required assumption
No independent pairing
Computation
Aggregate observed pairs
Interpretation
Observed joint table
A spatial workflow adds information by preserving where land-cover and soil classes occur together.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- EPA StreamCat
- USDA Soil Data Access
- Annual NLCD
- gNATSGO

## Slide 16
Independent pairing adds 1.88 curve-number units
The comparison uses identical raster marginals; only the pairing method changes.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Executed Earth Engine evidence, 6 August 2026
Marginals crossed independently
Difficult Run · 2019 · fair condition
Composite CN
77.6638
Land cover
Same raster marginal
Soils
Same raster marginal
Pairing
Assumed independent
Observed joint distribution
Difficult Run · 2019 · fair condition
Composite CN
75.7790
Land cover
Same raster marginal
Soils
Same raster marginal
Pairing
Measured jointly
The 1.8848-unit difference isolates the independence assumption. The earlier 4.50-unit result is a feasible tabular range, not this correction.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- evidence/gee-live/D2_executed_2026-08-06.ipynb
- prepared/difficult_run_gee_summary.json

## Slide 17
Soil source and spatial coverage remain reportable
Difficult Run demonstrates the scale of a source choice under the same land cover and condition.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Executed Earth Engine evidence; USDA SDA; HiHydroSoil v2.0
gNATSGO with SDA HSG lookup
CONUS map-unit interpretation
Analysis scale
30 m
Area with no HSG
21.27%
Composite CN
75.7790
Role
Workshop reference estimate
HiHydroSoil v2.0
Global modelled comparison
Analysis scale
250 m
Composite CN
83.9564
Difference
+8.1774 CN
Role
Source-sensitivity analysis
Report the soil asset, spatial scale, HSG interpretation, and mapped fraction with the composite estimate.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- evidence/gee-live/D2_executed_2026-08-06.ipynb
- USDA Soil Data Access
- HiHydroSoil v2.0

## Slide 18
Lab 2 · Estimate CN for a watershed
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Select the data pathway
Use a reference watershed or apply Earth Engine to a gage or outlet selected for analysis.
Review the boundary and inputs
Record delineation, land-cover product and year, soil source, resolution, and coverage.
Estimate the joint composite CN
Compare observed joint pairing with independent crossing and calculate the condition spread.
Prepare the report-out
Report CN, compositing convention, unmapped area, independence effect, and provenance.
Working time: 35 minutes. Both pathways use the same result schema and interpretation questions.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- notebooks/02_Build_CN_for_a_Watershed.ipynb
- docs/GEE_SETUP.md

## Slide 19
2
LAB 2 · REPORT-OUT
Which methodological uncertainty should accompany the headline curve-number estimate?
Use the condition spread, soil coverage, source sensitivity, and pairing effect to support the selection.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- notebooks/02_Build_CN_for_a_Watershed.ipynb

## Slide 20
Condition uncertainty exceeds the observed change
Difficult Run, 2001–2019; Annual NLCD and SDA-resolved gNATSGO.
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Executed Earth Engine trajectory, 6 August 2026
Difficult Run trajectory
Observed joint distribution · seven years
Scale comparison
Land-cover signal and methodological band
Measured change
+0.2876 CN
Mean condition spread
8.4473 CN
Spread / change
29.4×
Area with no HSG
21.27%
The temporal trajectory is interpretable only when the hydrologic-condition band and spatial coverage are reported with it.
Chart: Composite CN
| 2001 | 2004 | 2007 | 2010 | 2013 | 2016 | 2019
Poor | 80.4586 | 80.469 | 80.502 | 80.5198 | 80.5587 | 80.5994 | 80.6309
Fair | 75.4914 | 75.5693 | 75.6357 | 75.6826 | 75.7123 | 75.7491 | 75.779
Good | 71.8492 | 71.9757 | 72.0672 | 72.1359 | 72.1598 | 72.1948 | 72.2245
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- evidence/gee-live/D3_executed_2026-08-06.ipynb
- prepared/difficult_run_gee_trajectory.csv

## Slide 21
Table and fitted estimates differ
Asymptotic fits use measured rainfall and runoff; table estimates represent assigned basin characteristics.
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
USGS NWIS events; cnkit asymptotic fits
Difficult Run
USGS 01646000
Events
570
Table CN
75.5
Fitted CN∞
69.696
Fit R²
0.488
Accotink Creek
USGS 01654000
Events
563
Table CN
77.9
Fitted CN∞
78.902
Fit R²
0.083
The direction and strength of disagreement differ between basins; a universal table correction is not supported by these records.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- data/events_01646000.csv
- data/events_01654000.csv
- cnkit 1.1.0 fit_asymptotic

## Slide 22
Observed soil moisture stratifies event response
Difficult Run events grouped by NASA POWER root-zone wetness on the day before each event.
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NASA POWER GWETROOT; USGS NWIS event record
Driest third
Antecedent root-zone state
Events
204
Median wetness
0.49
Median event CN
74.97
Median runoff ratio
0.144
Wettest third
Antecedent root-zone state
Events
179
Median wetness
0.79
Median event CN
83.44
Median runoff ratio
0.285
Observed antecedent state provides a reproducible continuous variable for evaluating event response.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- data/soilmoisture_power_01646000.csv
- data/events_01646000.csv
- NASA POWER
- USGS NWIS

## Slide 23
Lab 3 · Evaluate change and uncertainty
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Plot the temporal trajectory
Place the fair-condition estimate inside the poor-to-good hydrologic-condition band.
Compare signal and assumptions
Calculate the land-cover change, mean condition spread, and their ratio.
Fit the measured gage record
Compare asymptotic fitted CN with the table estimate for both reference watersheds.
Evaluate antecedent state
Compare event response across the driest and wettest root-zone moisture thirds.
Working time: 25 minutes. Conclude with the six-line reporting statement in Notebook 03.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- notebooks/03_Change_and_Uncertainty.ipynb

## Slide 24
3
LAB 3 · REPORT-OUT
Does the observed temporal change exceed the uncertainty introduced by the method?
Compare the measured trajectory, hydrologic-condition spread, fitted gage evidence, and antecedent-state analysis.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- notebooks/03_Change_and_Uncertainty.ipynb

## Slide 25
A reproducible report states six items
4
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Equation and calibration
Curve-number relation, λ, and conversion basis.
Land cover
Product, year, class system, and resolution.
Soils
Source, HSG interpretation, and unmapped fraction.
Hydrologic condition
Selected condition and poor-to-good sensitivity.
Compositing convention
Distributed runoff, weighted CN, or weighted S.
Evidence and uncertainty
Measured change, fitted response, and assumption band.
Together these items define the minimum record needed to interpret and reproduce the estimate.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- notebooks/03_Change_and_Uncertainty.ipynb
- NRCS NEH-630 Chapters 7, 9, and 10

## Slide 26
Resources for continued application
4
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Earth Engine setup
Project registration, authentication, and Colab initialization.
Readiness notebook
Verifies cnkit, reference data, calculations, and Earth Engine access.
Three laboratory notebooks
Theory, spatial estimation, and evaluation in Google Colab.
Versioned data bundle
Reference inputs and recorded Earth Engine results with checksum.
cnkit 1.1.0
Core hydrology, delineation, Earth Engine, and workflow functions.
GitHub repository and portal
Slides, notebooks, data, source documentation, and build scripts.
Earth Engine supports watershed-specific application; the reference datasets support the same complete analytical sequence.
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- README.md
- docs/GEE_SETUP.md
- https://github.com/skp703/cnkit
- https://developers.google.com/earth-engine/guides/access

## Slide 27
4
SYNTHESIS
Report the curve number with its calibration, spatial provenance, compositing convention, and uncertainty.
A single value becomes interpretable when the measurement pathway and methodological assumptions are documented beside it.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Delivery note: connect this slide to the preceding analytical question.
[Sources]
- docs/V3_BLUEPRINT.md
- notebooks/01–03 participant reporting prompts