## Slide 1
0
2026 ASCE–EWRI Watershed Management Conference
Curve Number Hydrology and Remote Sensing Task Committees
Modern Curve Number Hydrology
Theory, spatial estimation, and Earth Observation applications
DURATION
Four hours
FORMAT
Lecture and three computational labs
CREDIT
4.0 PDH for the full workshop
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
John J. Ramirez-Avila, Mississippi State University | Saurav Kumar, Arizona State University
Notes: Frame the workshop as a four-hour sequence in which lecture establishes the model and analytical choices, and each notebook then makes those choices inspectable in code.
[Sources]
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 2
0
WORKSHOP PROBLEM
A curve number is an interpreted parameter—not a direct observation of land cover, soil, or runoff.
The workshop asks how model calibration, watershed data, spatial aggregation, and observed response jointly support a defensible estimate.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Use this as the intellectual contract for the workshop. The participant is not being taught to retrieve a single number; the participant is being taught to construct and audit an engineering parameter.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://doi.org/10.1061/(ASCE)0733-9437(1993)119:2(334)
[/Sources]

## Slide 3
Workshop instructors
The workshop integrates curve-number hydrology, spatial data, and engineering interpretation.
0
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
JJ
John J. Ramirez-Avila
Mississippi State University
Curve-number theory, rainfall–runoff interpretation, and the reporting implications of calibration and compositing.
SK
Saurav Kumar
Arizona State University
Earth Observation, watershed-scale estimation, temporal change, and reproducible computational workflows.
Participants may use verified reference datasets or apply the same analytical framework through Earth Engine to a selected watershed.
Notes: Introduce the complementary roles of curve-number theory, rainfall–runoff interpretation, Earth Observation, and reproducible computation.
[Sources]
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 4
Learning objectives
0
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
1
Explain the governing relation
Relate rainfall, initial abstraction, retention, runoff, curve number, and the initial-abstraction ratio.
2
Estimate CN from spatial data
Combine watershed boundaries, land cover, and hydrologic soil group with explicit provenance.
3
Evaluate methodological uncertainty
Compare observed change with hydrologic condition, soil coverage, calibration, and compositing choices.
4
Prepare a reproducible statement
Report the parameter, data sources, assumptions, spatial coverage, and evidence supporting interpretation.
Notes: Read the objectives as a progression: explain the model, estimate the parameter, evaluate methodological sensitivity, and prepare a reproducible statement.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 5
Workshop schedule
Three linked modules move from theory to spatial estimation and interpretation.
0
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
0:00
Welcome and orientation
10 min
0:10
Foundations: rainfall, runoff, and curve number
40 min
0:50
Lab 1 and report-out
30 min
1:20
Break
15 min
1:35
Earth Observation and spatial estimation
25 min
2:00
Lab 2 and report-out
45 min
2:45
Break
15 min
3:00
Change, uncertainty, and Lab 3
45 min
3:45
Reporting synthesis and close
15 min
4:00
End
15 min
Notes: Explain the teaching cadence. Slides introduce the problem and theory; the linked notebook immediately exposes the calculation, library operation, and analyst decision. Report-outs consolidate interpretation before the next module.
[Sources]
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 6
Two reference watersheds anchor the analysis
Long-record USGS gages provide contrasting physiographic and hydrologic settings.
0
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
USGS NWIS and NLDI; workshop data registry
Difficult Run near Great Falls, Virginia
USGS 01646000
Drainage area
57.8 square miles
Physiography
Piedmont
Record begins
1935
Workshop role
Complete spatial and gage analysis
Accotink Creek near Annandale, Virginia
USGS 01654000
Drainage area
23.9 square miles
Physiography
Coastal Plain
Record begins
1947
Workshop role
Contrasting fitted behavior
The reference datasets support the complete analytical sequence; Earth Engine extends the same method to a participant-selected watershed.
Notes: Use Difficult Run for the complete spatial and event analysis and Accotink Creek as a contrasting gage record. Participants may apply the same Earth Engine workflow to a selected CONUS watershed.
[Sources]
- https://waterdata.usgs.gov/nwis
- https://api.water.usgs.gov/docs
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 7
1
FOUNDATIONS · THEORY AND CALIBRATION
A curve number is inferred from rainfall–runoff behavior; it is not a directly observed property of a pixel.
The spatial inputs inform parameter estimation. The runoff relation, calibration convention, and observed response determine its interpretation.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Transition from workshop framing to the governing rainfall–runoff relation and its calibration.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://doi.org/10.1061/(ASCE)0733-9437(1993)119:2(334)
[/Sources]

## Slide 8
The runoff equation contains two linked parameters
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Rainfall, P
Observed storm depth for the event.
Initial abstraction, Iₐ = λS
Loss before runoff begins; λ is part of the calibration.
Potential retention, S
S = 1000/CN − 10 inches.
Direct runoff, Q
Q = (P − Iₐ)² / (P − Iₐ + S) for P > Iₐ; otherwise Q = 0.
Changing λ changes the curve-number scale. Report λ and CN together.
Notes: Develop the model in the order shown: observed rainfall, initial abstraction, potential retention, then direct runoff. Emphasize the piecewise threshold and the need to state lambda with CN.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
[/Sources]

## Slide 9
Initial abstraction controls the onset of modeled runoff
Example for CN 70 and λ = 0.20: S = 4.286 in and Iₐ = 0.857 in.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NEH-630 Subpart H; cnkit runoff calculation
Event below the threshold
P = 0.75 in < Iₐ
Rainfall depth
0.750 in
Initial abstraction
0.857 in
Modeled direct runoff
0.000 in
Interpretation
Threshold not crossed
Event above the threshold
P = 1.50 in > Iₐ
Rainfall depth
1.500 in
Excess above Iₐ
0.643 in
Modeled direct runoff
0.084 in
Interpretation
Nonlinear response begins
A zero value below Iₐ is a statement about modeled direct runoff, not a claim that no water moves within the watershed.
Notes: Write the values on the board if helpful. The calculation demonstrates why small storms and lower-CN subareas are especially sensitive to the abstraction convention.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://github.com/skp703/cnkit
[/Sources]

## Slide 10
Lambda and curve number form a calibration pair
Changing one without converting the other changes the model response.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NEH-630 Ch. 10; Woodward et al. (2003)
Conventional formulation
Initial-abstraction ratio λ = 0.20
Curve number
75.5
Three-inch storm
0.988 in runoff
Calibration basis
NEH/TR-55 tables
Retention
S = 3.245 in
Alternative formulation
Initial-abstraction ratio λ = 0.05
Converted curve number
66.0
Three-inch storm
0.953 in runoff
Calibration basis
Empirical conversion
Interpretation
A different CN scale
A reported curve number is incomplete unless its initial-abstraction convention is stated.
Notes: The conventional and alternative formulations use different CN scales. A curve number calibrated with one lambda should be converted or refitted before use with another lambda.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://doi.org/10.1061/40685(2003)308
[/Sources]

## Slide 11
Table and event CNs answer different questions
They may be compared, but they should not be treated as interchangeable observations.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NEH-630; Hawkins (1993); USGS NWIS
Table-derived CN
Assigned from watershed attributes
Primary inputs
Land cover, HSG, condition
Evidence type
Spatial classification
Analytical role
Design baseline
Main sensitivities
Mapping and lookup choices
Event-derived CN
Inferred from measured response
Primary inputs
Rainfall P and runoff Q
Evidence type
Storm observations
Analytical role
Performance evidence
Main sensitivities
Separation, λ, and fit form
Agreement is evidence of consistency; disagreement is a diagnostic that must be interpreted in context.
Notes: Do not present the event-derived value as the truth and the table value as an error. They arise from different measurement pathways and support different inferences.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://doi.org/10.1061/(ASCE)0733-9437(1993)119:2(334)
- https://waterdata.usgs.gov/nwis
[/Sources]

## Slide 12
Curve number is inferred from storm response
Measured rainfall and runoff provide the evidence used to evaluate an assigned table value.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
USGS NWIS; events_01646000.csv; cnkit 1.1.0
Difficult Run storm events
570 separated events · 1990–2026
Parameter estimation
NRCS runoff relation
Observed variables
Rainfall P and runoff Q
Model parameters
Curve number CN and λ
Asymptotic fit
CN∞ = 69.7
Table estimate
CN = 75.5
The fitted estimate is obtained from measured events; the table estimate is assigned from land cover, soil, and hydrologic condition.
Chart: Runoff, in
Notes: Use the scatter to show that event response is heterogeneous and that fitted CN is an inference from the event cloud rather than a direct property of the watershed.
[Sources]
- https://waterdata.usgs.gov/nwis
- https://doi.org/10.1061/(ASCE)0733-9437(1993)119:2(334)
- https://github.com/skp703/cnkit
[/Sources]

## Slide 13
Asymptotic fitting tests whether event CN stabilizes
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Prepare the events
Separate rainfall and direct runoff consistently; retain the event-selection record.
Invert the equation
Compute an event CN from each valid P–Q pair at the stated λ.
Fit a named response
Estimate the Hawkins standard asymptote from event CN versus rainfall depth.
Evaluate adequacy
Inspect event count, pattern, residual behavior, and R² before interpreting CN∞.
A fitted asymptote is evidence about the measured record; it does not erase uncertainty in event separation or model structure.
Notes: Explain each operation before showing the notebook function. The library performs inversion and nonlinear fitting; the analyst controls event selection, lambda, fit interpretation, and the evidentiary claim.
[Sources]
- https://doi.org/10.1061/(ASCE)0733-9437(1993)119:2(334)
- https://waterdata.usgs.gov/nwis
- https://github.com/skp703/cnkit
[/Sources]

## Slide 14
Compositing order changes runoff
One inch of rainfall over 60% connected impervious cover and 40% woods.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NEH-630 Ch. 9; TR-55 Worksheet 2; cnkit calculation
Three valid calculations
CN 98 impervious · CN 55 woods
Distributed runoff
0.4745 in
Area-weighted CN
0.0949 in
Area-weighted S
0.0277 in
Maximum ratio
17×
Why the results diverge
The wooded subarea has Iₐ = 1.64 in
Storm depth
1.00 in
Distributed sequence
Compute Q, then average
Lumped sequence
Average parameter, then Q
Engineering choice
Document the representation
The arithmetic is correct in each case; the calculations represent different spatial models.
Notes: The example isolates the order-of-operations issue. Computing runoff within subareas and then averaging is not equivalent to averaging CN or retention first because the runoff relation is nonlinear and piecewise.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://github.com/skp703/cnkit
[/Sources]

## Slide 15
Compositing diverges near abstraction thresholds
Hold CN values and area fractions fixed; vary only storm depth P.
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notebook 01 controlled calculation; NEH-630
Near-threshold example
One-inch storm over CN 98 and CN 55 subareas
Distributed runoff
0.4745 in
Area-weighted CN
0.0949 in
Area-weighted S
0.0277 in
Maximum ratio
17×
Why the gap changes with P
Subareas cross Iₐ at different storm depths
Small storms
Threshold effects dominate
Larger storms
More subareas generate Q
Controlled comparison
Only rainfall changes
Reporting implication
State the representation
The chosen compositing convention is part of the model definition and should remain visible in design-runoff reporting.
Notes: Use the storm-depth plot in Notebook 01 to extend this slide. The lecture establishes why the curves separate; the notebook lets participants inspect how the separation changes continuously with P.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://github.com/skp703/cnkit
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 16
Lab 1 · Understand and audit the equation
1
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Run the setup and comparison
Open Notebook 01, execute the reference calculations, and inspect the three-inch storm table.
Evaluate the lambda pair
Explain why λ = 0.20 and λ = 0.05 require different curve-number scales.
Calculate the weighting example
Compare distributed runoff, weighted CN, and weighted S for the one-inch storm.
Prepare the report-out
Select a compositing convention and identify the evidence supporting that choice.
Working time: 20 minutes. Record the three runoff depths and one concise interpretation.
Notes: Move to Notebook 01. The notebook contains the written equations, verification assertions, compositing calculations, event inversion, asymptotic fit, and a method audit that distinguishes library operations from analyst decisions.
[Sources]
- https://github.com/skp703/cn-workshop-2026
- https://github.com/skp703/cnkit
[/Sources]

## Slide 17
1
LAB 1 · REPORT-OUT
Which compositing convention would you report for a heterogeneous watershed, and what evidence supports that choice?
State the calculation sequence, the resulting runoff depth, and the spatial representation implied by the method.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Ask participants to name the calculation sequence, not only the preferred number. The report-out should connect the runoff depth to the spatial representation implied by the convention.
[Sources]
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 18
2
EARTH OBSERVATION · SPATIAL ESTIMATION
A watershed curve number is constructed from a boundary, land cover, soil interpretation, lookup convention, and spatial aggregation.
Earth Engine supplies watershed-specific spatial measurements; the same hydrologic arithmetic is available through the versioned reference pathway.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Transition from the event model to the spatial measurement problem. The central question becomes how each raster and table is transformed into a traceable watershed parameter.
[Sources]
- https://developers.google.com/earth-engine/guides/client_server
- https://www.usgs.gov/centers/eros/science/about-annual-nlcd
- https://www.nrcs.usda.gov/sites/default/files/2025-01/NCSS-raster-soil-data-products.pdf
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 19
Earth Observation supports spatial estimation
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Define the watershed
Use a verified boundary, USGS gage number, or outlet coordinates.
Measure land cover
Select the product, year, resolution, and class system explicitly.
Resolve hydrologic soil group
Link mapped soil units to HSG and quantify the area with no assignment.
Aggregate the joint distribution
Align land cover and soil spatially, then summarize observed class pairs.
Reference datasets provide verified outputs; Earth Engine applies the same sequence to a selected watershed.
Notes: Preview the complete sequence before discussing software: define the watershed, measure land cover, resolve HSG, and aggregate observed land-cover–soil pairs.
[Sources]
- https://api.water.usgs.gov/docs
- https://www.usgs.gov/centers/eros/science/about-annual-nlcd
- https://www.nrcs.usda.gov/sites/default/files/2025-01/NCSS-raster-soil-data-products.pdf
- https://github.com/skp703/cnkit
[/Sources]

## Slide 20
Watershed delineation begins at a defined outlet
A gage identifier and an arbitrary coordinate use related but distinct USGS routes.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
USGS NLDI API; cnkit.delineate
Gage route
watershed_from_gage(gage)
Identifier
Eight-digit USGS gage
NLDI action
Resolve monitoring location
Boundary action
Aggregate upstream basin
Primary use
Gage-based analysis
Outlet-coordinate route
watershed_from_point(lat, lon)
Identifier
Latitude and longitude
NLDI action
Snap to NHDPlusV2 flowline
Boundary action
Split-catchment upstream
Primary use
Selected outlet analysis
Record the requested point, snapped point, delineation method, source dataset, area, and warnings with the returned geometry.
Notes: Stress that the user selects the hydrologic meaning of the outlet. The library performs service requests and geometry assembly; it does not decide whether a gage or coordinate represents the intended control point.
[Sources]
- https://api.water.usgs.gov/docs
- https://github.com/skp703/cnkit
[/Sources]

## Slide 21
The delineation library exposes each operation
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Resolve or snap the outlet
Translate a gage or coordinate into a network-connected hydrolocation.
Navigate upstream
Request the NHDPlusV2 basin or split-catchment aggregation from NLDI.
Construct the record
Return GeoJSON, area, request and snapped points, source, method, and warnings.
Retain fallback provenance
If the selected route changes, preserve the method used rather than hiding the substitution.
Delineation is a USGS web-service operation; Earth Engine authentication is a separate later step.
Notes: Walk through the function output fields before showing a map. This prepares participants to interpret the `Watershed` object rather than treating it as an opaque polygon.
[Sources]
- https://api.water.usgs.gov/docs
- https://github.com/skp703/cnkit
[/Sources]

## Slide 22
A watershed boundary requires verification
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Outlet location
Confirm the requested and snapped points represent the intended control point.
Drainage area
Compare calculated area with published gage metadata or another trusted source.
Upstream extent
Inspect ridges, tributaries, nested basins, and obvious network discontinuities.
Geometry validity
Check coordinate order, closure, multipart geometry, and unreasonable vertex artifacts.
Method provenance
Retain NLDI route, dataset, request parameters, timestamp, and warnings.
Map context
Plot the boundary and outlet over a referenced basemap before raster analysis.
A successful web request is not equivalent to a verified watershed.
Notes: Notebook 02 performs the area comparison and displays the boundary on a USGS Topo basemap. Participants should record any discrepancy and decide whether it is acceptable for the intended analysis.
[Sources]
- https://api.water.usgs.gov/docs
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 23
Earth Engine supports a selected-watershed analysis
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Register access
Use an Earth Engine-enabled Google Cloud project associated with the participant.
Open in Colab
The Python API is available in Colab; import, authenticate, and initialize the session.
Verify the project
Run the readiness check and confirm a simple server-side calculation returns 42.
Select a watershed
Provide a USGS gage number or outlet coordinates for the live application.
Use versioned evidence
The reference pathway reproduces the complete analysis with recorded watershed outputs.
Keep one result schema
Both pathways report boundary, inputs, CN, unmapped area, assumptions, and provenance.
Earth Engine is an application pathway; the theory, calculations, and interpretation are fully available in every notebook.
Notes: Point participants to the setup guide and Readiness Check. Present the two pathways as different data-acquisition routes that share the same scientific questions and reporting schema.
[Sources]
- https://developers.google.com/earth-engine/guides/access
- https://developers.google.com/earth-engine/guides/auth
- https://developers.google.com/earth-engine/guides/python_install-colab
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 24
Earth Engine executes a deferred request graph
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Define objects locally
Python statements construct deferred Earth Engine images, geometries, and reducers.
Build the request graph
Filter collections, select bands, clip to the basin, mask, and specify reductions.
Execute remotely
Earth Engine evaluates the graph against cloud-hosted data at the stated scale.
Retrieve summaries
Use getInfo only for compact tables and scalars returned to the notebook.
cnkit.gee organizes the request; the analyst still selects boundary, product, year, scale, soil source, and interpretation.
Notes: This slide explains why notebook cells can run quickly while the data remain remote. Avoid repeated retrieval of large objects; request compact histograms and statistics that support the watershed calculation.
[Sources]
- https://developers.google.com/earth-engine/guides/client_server
- https://github.com/skp703/cnkit
[/Sources]

## Slide 25
The Basin object binds geometry and execution settings
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Boundary
Converts the verified watershed GeoJSON into an Earth Engine geometry.
Project
Initializes requests through the participant’s Earth Engine-enabled Cloud project.
Analysis scale
Retains the working pixel size used by reductions and comparisons.
Pixel policy
Controls reprojection, drainage treatment, and compatible reductions.
Cache and retrieval
Avoids repeated service work and retrieves only compact summaries.
Method record
Carries selected inputs into land-cover, soil, joint-distribution, and trajectory methods.
Convenience methods orchestrate operations; they do not remove the need to inspect boundary, inputs, coverage, and assumptions.
Notes: Use `Basin` as a transparent container, not a black box. Notebook 02 shows the lower-level methods before calling the composite convenience method.
[Sources]
- https://developers.google.com/earth-engine/guides/client_server
- https://github.com/skp703/cnkit
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 26
Land-cover class area and imperviousness differ
Both are useful; neither should be substituted for the other.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
USGS Annual NLCD Collection 1.2; cnkit.gee
Categorical land cover
Basin.landcover(year)
Source
Annual NLCD class band
Operation
Clip, mask, frequency histogram
Output
Area by NLCD class
Use in CN
Lookup-table class index
Fractional imperviousness
Basin.impervious(year)
Source
Annual impervious band
Operation
Clip and mean reduction
Output
Mean impervious percent
Use in interpretation
Development intensity evidence
Report product, collection, year, class system, resolution, mask, and watershed denominator with the land-cover summary.
Notes: Explain that a developed land-cover class is categorical, whereas imperviousness is a continuous percent. The library reduces them separately and preserves both for interpretation.
[Sources]
- https://www.usgs.gov/centers/eros/science/about-annual-nlcd
- https://github.com/skp703/cnkit
[/Sources]

## Slide 27
Hydrologic soil group is an interpreted class
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Group A
High infiltration potential and generally lower runoff potential when thoroughly wetted.
Group B
Moderate infiltration and runoff potential under the standard interpretation.
Group C
Slow infiltration and greater runoff potential than groups A or B.
Group D
Very slow infiltration or high runoff potential under the table framework.
Dual groups
A/D, B/D, and C/D depend on drainage convention; retain the original designation.
Unmapped area
Map units without a resolved HSG remain explicit rather than silently reassigned.
State the soil source, HSG interpretation, drainage convention, spatial scale, and mapped fraction.
Notes: Keep the explanation tied to the CN lookup. HSG summarizes infiltration and transmission behavior used by the tables; it is not a direct measurement of event infiltration at a pixel.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://www.nrcs.usda.gov/sites/default/files/2025-01/NCSS-raster-soil-data-products.pdf
- https://sdmdataaccess.sc.egov.usda.gov/WebServiceHelp.aspx
[/Sources]

## Slide 28
gNATSGO geometry is joined to Soil Data Access
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Measure map-unit keys
Reduce the 30 m gNATSGO map-unit-key raster within the verified basin.
Resolve attributes once
Query Soil Data Access for dominant-condition HSG linked to each map-unit key.
Reclassify in Earth Engine
Map the lookup back to the basin raster while retaining dual groups and missing values.
Summarize coverage
Return HSG areas and the fraction for which no assignment was available.
The raster defines where map units occur; Soil Data Access supplies the tabular interpretation used by the lookup.
Notes: Describe the two-source join explicitly. It prevents participants from assuming that the gNATSGO raster already contains the final HSG category used in the CN table.
[Sources]
- https://www.nrcs.usda.gov/sites/default/files/2025-01/NCSS-raster-soil-data-products.pdf
- https://sdmdataaccess.sc.egov.usda.gov/WebServiceHelp.aspx
- https://github.com/skp703/cnkit
[/Sources]

## Slide 29
Soil source and spatial coverage remain reportable
Difficult Run demonstrates the scale of a source choice under the same land cover and condition.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Executed Earth Engine evidence; USDA SDA; HiHydroSoil v2.0
gNATSGO with SDA HSG lookup
CONUS map-unit interpretation
Analysis scale
30 m
Area with no HSG
21.27%
Composite CN
75.7790
Role
Workshop reference estimate
HiHydroSoil v2.0
Global modelled comparison
Analysis scale
250 m
Composite CN
83.9564
Difference
+8.1774 CN
Role
Source-sensitivity analysis
Report the soil asset, spatial scale, HSG interpretation, and mapped fraction with the composite estimate.
Notes: The Difficult Run result demonstrates that soil source and scale can shift the composite more than the measured land-cover trajectory. Treat the global modeled soil product as a sensitivity comparison, not as an interchangeable replacement.
[Sources]
- https://www.nrcs.usda.gov/sites/default/files/2025-01/NCSS-raster-soil-data-products.pdf
- https://sdmdataaccess.sc.egov.usda.gov/WebServiceHelp.aspx
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 30
Marginal and joint distributions differ
The distinction is spatial association, not simply data volume.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
EPA StreamCat; USDA SDA; Annual NLCD; gNATSGO
Marginal distributions
Land-cover and soil percentages are separate
Spatial association
Not retained
Required assumption
Independent pairing
Computation
Cross all classes
Interpretation
Synthetic joint table
Joint spatial distribution
Land-cover–soil pairs share a location
Spatial association
Measured pixel by pixel
Required assumption
No independent pairing
Computation
Aggregate observed pairs
Interpretation
Observed joint table
A spatial workflow adds information by preserving where land-cover and soil classes occur together.
Notes: A marginal table retains only separate class totals. The pixelwise joint histogram preserves which land-cover and HSG classes share a location and therefore contributes additional spatial evidence.
[Sources]
- https://www.usgs.gov/centers/eros/science/about-annual-nlcd
- https://www.nrcs.usda.gov/sites/default/files/2025-01/NCSS-raster-soil-data-products.pdf
- https://github.com/skp703/cnkit
[/Sources]

## Slide 31
Independent pairing adds 1.88 curve-number units
The comparison uses identical raster marginals; only the pairing method changes.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Executed Earth Engine evidence, 6 August 2026
Marginals crossed independently
Difficult Run · 2019 · fair condition
Composite CN
77.6638
Land cover
Same raster marginal
Soils
Same raster marginal
Pairing
Assumed independent
Observed joint distribution
Difficult Run · 2019 · fair condition
Composite CN
75.7790
Land cover
Same raster marginal
Soils
Same raster marginal
Pairing
Measured jointly
The 1.8848-unit difference isolates the independence assumption. The earlier 4.50-unit result is a feasible tabular range, not this correction.
Notes: The comparison holds the raster marginals fixed and changes only the pairing method. The 1.8848-unit difference therefore isolates the independence assumption for this boundary, year, scale, soil source, and condition.
[Sources]
- https://github.com/skp703/cn-workshop-2026
- https://github.com/skp703/cnkit
[/Sources]

## Slide 32
The lookup assigns CN to each spatial class pair
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Land-cover class
Translate Annual NLCD classes into the adopted TR-55 or NEH category crosswalk.
Hydrologic soil group
Index A, B, C, D, or the documented treatment of a dual group.
Hydrologic condition
Select poor, fair, or good from management and cover evidence—not from NLCD alone.
Local lookup value
Attach the table CN to each mapped land-cover–soil spatial unit.
Unmapped pair
Retain null values when the crosswalk or HSG interpretation does not support a lookup.
Audit output
Rank local area contributions and inspect dominant or unresolved combinations.
The library indexes the adopted table; the analyst establishes the crosswalk and evidentiary basis for hydrologic condition.
Notes: Hydrologic condition is often the largest controllable lookup sensitivity. Ask participants what field or management evidence would support poor, fair, or good for the dominant classes.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://github.com/skp703/cnkit
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 33
Aggregation retains the compositing convention
cnkit returns multiple composites and the unmapped fraction so the choice remains auditable.
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NEH-630; cnkit.lookup.composite_from_areas
Area-weighted CN
Average local curve numbers
Calculation
Σ AᵢCNᵢ / Σ Aᵢ
Hydrologic meaning
One lumped CN parameter
Runoff step
Apply Q after averaging CN
Required record
Mapped area and convention
Area-weighted retention
Average S derived from local CN
Calculation
Σ AᵢSᵢ / Σ Aᵢ
Hydrologic meaning
One lumped retention value
Runoff step
Convert S and apply Q
Not returned here
Distributed runoff by subarea
A composite CN is a parameter. A runoff depth additionally requires storm depth, lambda, and the stated spatial representation.
Notes: Connect this slide back to Lab 1. `composite_from_areas` reports weighted-CN and weighted-retention summaries; a fully distributed runoff calculation is a separate operation.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://github.com/skp703/cnkit
[/Sources]

## Slide 34
Design runoff is the final step of a documented chain
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Select the storm
Use a stated NOAA Atlas 14 duration, annual-exceedance interval, location, and depth.
Select the model pair
Use the reported composite CN with the matching initial-abstraction ratio λ.
Apply the equation
Compute runoff depth only after boundary, spatial inputs, lookup, and aggregation are fixed.
Assemble provenance
Report boundary, products, years, scale, HSG source, condition, coverage, convention, storm, and result.
For the Difficult Run reference analysis, the versioned 10-year 24-hour depth is 4.78 in at the gage location.
Notes: The notebook produces a structured provenance record beside the design runoff. Explain that rainfall at a point, basin centroid, or areal-reduction product is a separate choice that should be visible.
[Sources]
- https://www.weather.gov/owp/hdsc
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 35
Lab 2 · Estimate CN for a watershed
2
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Select the data pathway
Use a reference watershed or apply Earth Engine to a gage or outlet selected for analysis.
Review the boundary and inputs
Record delineation, land-cover product and year, soil source, resolution, and coverage.
Estimate the joint composite CN
Compare observed joint pairing with independent crossing and calculate the condition spread.
Prepare the report-out
Report CN, compositing convention, unmapped area, independence effect, and provenance.
Working time: 35 minutes. Both pathways use the same result schema and interpretation questions.
Notes: Move to Notebook 02. Participants first inspect watershed identification, delineation, verification, land cover, HSG, joint pairing, lookup, aggregation, independence sensitivity, and design runoff before using the convenience method.
[Sources]
- https://github.com/skp703/cn-workshop-2026
- https://github.com/skp703/cnkit
- https://developers.google.com/earth-engine/guides/auth
[/Sources]

## Slide 36
2
LAB 2 · REPORT-OUT
Which methodological uncertainty should accompany the headline curve-number estimate?
Use the condition spread, soil coverage, source sensitivity, and pairing effect to support the selection.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: The report-out should name one uncertainty that belongs beside the headline estimate and justify why it is methodologically material for the selected watershed.
[Sources]
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 37
3
CHANGE · CALIBRATION · ANTECEDENT STATE
A temporal difference is interpretable only after the changing signal is compared with uncertainty introduced by the method.
The analysis holds boundary, soils, lookup, condition, scale, and compositing constant while land-cover year changes, then compares spatial, event, and antecedent-state evidence.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Transition from building a single estimate to evaluating change. Emphasize controlled comparison: the study design must state what changes and what is held fixed.
[Sources]
- https://www.usgs.gov/centers/eros/science/about-annual-nlcd
- https://doi.org/10.1061/(ASCE)0733-9437(1993)119:2(334)
- https://power.larc.nasa.gov/docs/services/api/temporal/daily/
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 38
A defensible trajectory changes one input at a time
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Changing input
Annual NLCD year supplies the land-cover trajectory from 2001 through 2019.
Boundary held fixed
Use one verified Difficult Run geometry for every year.
Soils held fixed
Use the same gNATSGO and Soil Data Access HSG interpretation.
Lookup held fixed
Keep the crosswalk, hydrologic condition, and lambda convention constant.
Scale held fixed
Use the same raster resolution, masks, and coverage accounting.
Aggregation held fixed
Use the observed joint distribution and the same composite convention every year.
Without these controls, a change in CN may reflect a workflow change rather than a watershed change.
Notes: Notebook 03 prints this control statement before loading the trajectory and again before the optional live Earth Engine calculation.
[Sources]
- https://www.usgs.gov/centers/eros/science/about-annual-nlcd
- https://github.com/skp703/cn-workshop-2026
- https://github.com/skp703/cnkit
[/Sources]

## Slide 39
Condition uncertainty exceeds the observed change
Difficult Run, 2001–2019; Annual NLCD and SDA-resolved gNATSGO.
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Executed Earth Engine trajectory, 6 August 2026
Difficult Run trajectory
Observed joint distribution · seven years
Scale comparison
Land-cover signal and methodological band
Measured change
+0.2876 CN
Mean condition spread
8.4473 CN
Spread / change
29.4×
Area with no HSG
21.27%
The temporal trajectory is interpretable only when the hydrologic-condition band and spatial coverage are reported with it.
Chart: Composite CN
| 2001 | 2004 | 2007 | 2010 | 2013 | 2016 | 2019
Poor | 80.4586 | 80.469 | 80.502 | 80.5198 | 80.5587 | 80.5994 | 80.6309
Fair | 75.4914 | 75.5693 | 75.6357 | 75.6826 | 75.7123 | 75.7491 | 75.779
Good | 71.8492 | 71.9757 | 72.0672 | 72.1359 | 72.1598 | 72.1948 | 72.2245
Notes: The fair-condition trajectory changes by 0.2876 CN units, while the mean poor-to-good spread is 8.4473 units. The methodological band is 29.4 times the measured temporal signal.
[Sources]
- https://github.com/skp703/cn-workshop-2026
- https://github.com/skp703/cnkit
[/Sources]

## Slide 40
Table and fitted estimates differ
Asymptotic fits use measured rainfall and runoff; table estimates represent assigned basin characteristics.
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
USGS NWIS events; cnkit asymptotic fits
Difficult Run
USGS 01646000
Events
570
Table CN
75.5
Fitted CN∞
69.696
Fit R²
0.488
Accotink Creek
USGS 01654000
Events
563
Table CN
77.9
Fitted CN∞
78.902
Fit R²
0.083
The direction and strength of disagreement differ between basins; a universal table correction is not supported by these records.
Notes: Difficult Run and Accotink Creek do not show a common direction or strength of disagreement between table and fitted estimates. A universal correction is not supported by these two records.
[Sources]
- https://waterdata.usgs.gov/nwis
- https://doi.org/10.1061/(ASCE)0733-9437(1993)119:2(334)
- https://github.com/skp703/cnkit
[/Sources]

## Slide 41
Antecedent-state measures are not equivalent
They can be compared on the same event dates, but their categories should not be relabeled as equivalent.
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NEH-630/NEH-4; NASA POWER Daily API and MERRA-2
Rainfall-history convention
Antecedent rainfall accumulation
Variable
Prior multi-day precipitation
Threshold basis
Seasonal historical classes
Interpretation
Discrete runoff-condition proxy
Primary limitation
Does not observe soil water
Root-zone wetness convention
NASA POWER GWETROOT percentile
Variable
Modeled root-zone wetness
Threshold basis
Event-date empirical quantiles
Interpretation
Continuous antecedent-state proxy
Primary limitation
Coarse reanalysis support
Use both as reproducible descriptors; do not redefine NRCS antecedent runoff-condition classes with NASA wetness percentiles.
Notes: Explain that the notebook compares classifications rather than declaring one universally superior. The event-response summaries then test whether the continuous wetness rank is hydrologically informative for this record.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://power.larc.nasa.gov/docs/services/api/temporal/daily/
- https://ntrs.nasa.gov/api/citations/20150019760/downloads/20150019760.pdf
[/Sources]

## Slide 42
Observed soil moisture stratifies event response
Difficult Run events grouped by NASA POWER root-zone wetness on the day before each event.
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
NASA POWER GWETROOT; USGS NWIS event record
Driest third
Antecedent root-zone state
Events
204
Median wetness
0.49
Median event CN
74.97
Median runoff ratio
0.144
Wettest third
Antecedent root-zone state
Events
179
Median wetness
0.79
Median event CN
83.44
Median runoff ratio
0.285
Observed antecedent state provides a reproducible continuous variable for evaluating event response.
Notes: The wettest third has higher median event CN and runoff ratio than the driest third. Treat this as stratified evidence for the Difficult Run event record, not as a replacement CN table.
[Sources]
- https://power.larc.nasa.gov/docs/services/api/temporal/daily/
- https://ntrs.nasa.gov/api/citations/20150019760/downloads/20150019760.pdf
- https://waterdata.usgs.gov/nwis
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 43
Lab 3 · Evaluate change and uncertainty
3
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Plot the temporal trajectory
Place the fair-condition estimate inside the poor-to-good hydrologic-condition band.
Compare signal and assumptions
Calculate the land-cover change, mean condition spread, and their ratio.
Fit the measured gage record
Compare asymptotic fitted CN with the table estimate for both reference watersheds.
Evaluate antecedent state
Compare event response across the driest and wettest root-zone moisture thirds.
Working time: 25 minutes. Conclude with the six-line reporting statement in Notebook 03.
Notes: Move to Notebook 03. Participants evaluate the spatial trajectory, compare signal with the hydrologic-condition band, fit the measured gage record, and compare antecedent-state conventions.
[Sources]
- https://github.com/skp703/cn-workshop-2026
- https://github.com/skp703/cnkit
[/Sources]

## Slide 44
3
LAB 3 · REPORT-OUT
Does the observed temporal change exceed the uncertainty introduced by the method?
Compare the measured trajectory, hydrologic-condition spread, fitted gage evidence, and antecedent-state analysis.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Ask whether the observed temporal signal exceeds methodological uncertainty and require evidence from the trajectory, condition band, fitted record, and antecedent-state analysis.
[Sources]
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 45
A reproducible report states six items
4
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Equation and calibration
Curve-number relation, λ, and conversion basis.
Land cover
Product, year, class system, and resolution.
Soils
Source, HSG interpretation, and unmapped fraction.
Hydrologic condition
Selected condition and poor-to-good sensitivity.
Compositing convention
Distributed runoff, weighted CN, or weighted S.
Evidence and uncertainty
Measured change, fitted response, and assumption band.
Together these items define the minimum record needed to interpret and reproduce the estimate.
Notes: Use the six categories as the minimum metadata needed to interpret and reproduce a reported curve number. A number without this record is analytically incomplete.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://github.com/skp703/cn-workshop-2026
[/Sources]

## Slide 46
A complete result is a structured scientific claim
4
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Parameter
Difficult Run 2019 fair-condition composite CN = 75.7790; λ = 0.20.
Spatial basis
NLDI boundary; Annual NLCD; 30 m gNATSGO with SDA HSG; observed joint pairs.
Design response
Apply the stated CN–λ pair to the 4.78 in NOAA Atlas 14 10-year 24-hour depth.
Uncertainty record
21.27% no mapped HSG; +1.8848 CN independence effect; 8.4473 CN mean condition spread.
The result remains interpretable because the calibration, measurement pathway, coverage, aggregation, rainfall basis, and sensitivity evidence are stated together.
Notes: This is a reporting example, not a universal wording template. Ask participants to identify which parts are measured, assigned, modeled, or calculated.
[Sources]
- https://github.com/skp703/cn-workshop-2026
- https://api.water.usgs.gov/docs
- https://www.usgs.gov/centers/eros/science/about-annual-nlcd
- https://www.nrcs.usda.gov/sites/default/files/2025-01/NCSS-raster-soil-data-products.pdf
- https://www.weather.gov/owp/hdsc
[/Sources]

## Slide 47
Resources for continued application
4
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Earth Engine setup
Project registration, authentication, and Colab initialization.
Readiness notebook
Verifies cnkit, reference data, calculations, and Earth Engine access.
Three laboratory notebooks
Theory, spatial estimation, and evaluation in Google Colab.
Versioned data bundle
Reference inputs and recorded Earth Engine results with checksum.
cnkit 1.1.0
Core hydrology, delineation, Earth Engine, and workflow functions.
GitHub repository and portal
Slides, notebooks, data, source documentation, and build scripts.
Earth Engine supports watershed-specific application; the reference datasets support the same complete analytical sequence.
Notes: Point participants to the setup guide, readiness check, notebooks, data bundle, cnkit documentation, public repository, and workshop portal. The repository is the canonical versioned source.
[Sources]
- https://github.com/skp703/cn-workshop-2026
- https://github.com/skp703/cnkit
- https://developers.google.com/earth-engine/guides/access
- https://developers.google.com/earth-engine/guides/python_install-colab
[/Sources]

## Slide 48
4
SYNTHESIS
Report the curve number with its calibration, spatial provenance, compositing convention, and uncertainty.
A single value becomes interpretable when the measurement pathway and methodological assumptions are documented beside it.
Modern Curve Number Hydrology | ASCE–EWRI 2026 | Ramirez-Avila and Kumar
Notes: Close by returning to the opening problem. A curve number becomes defensible when calibration, spatial provenance, aggregation, coverage, and uncertainty accompany the value.
[Sources]
- https://directives.nrcs.usda.gov/sites/default/files2/1754923466/Subpart%20H%20%E2%80%93%20Estimation%20of%20Direct%20Runoff%20from%20Storm%20Rainfall.pdf
- https://doi.org/10.1061/(ASCE)0733-9437(1993)119:2(334)
- https://github.com/skp703/cn-workshop-2026
[/Sources]